Please copy and distribute to superintendents and all personnel affected.

Equipment:	Hydraulic Valves Pre-set for Construction Operation

Information:	Effective immediately, all hydraulic valves leaving the Walnut manufacturing facility will be pre-adjusted for a construction speed of 50 fpm.  The 50 fpm construction speed applies to both the “UP” and “DOWN” directions.

The valve must be restored to its default settings prior to adjusting the valve for normal operation.  Restore the valve adjustments in accordance with the valve setting sheet located inside the controller.  The “lowering speed adjuster” will have to be turned out and the “low pressure adjuster” will have to be turned out to restore the valve to default.

CAUTION:  The car or car frame MUST be either landed on the buffers or be in flight when the “lowering speed adjuster” is rotated.  Manipulating this adjuster under pressure in a static condition may damage the valve!

The following label will be attached to the valve in the factory after the valve has been set to 50 fpm: