Please copy and distribute to superintendents and all personnel affected.

Equipment:	Twinpost Telescopic Jacks

Information:	All Twinpost Telescopic Jack jobs shipped after June, 2005 will be shipped without static sensors.  Three landing jobs will still require dynamic sensors.  Controllers will be shipped with V4R2 Generic Software.  Resync will be controlled on a timed interval (Adj 033 for 24, 48, or 72 hours) and a new Motor start counter (Adj 044).  Adjustment JRT will continue to be used in conjunction with Adjustment 033 to select the time of Day that resync will occur. The car will also home to the bottom landing at least once every six hours.

2 Stop cars: 	No static or dynamic sensors will be required. The jacks will resync once every 24, 48 or 72 hrs (Adj 033).

3 Stop and greater: Only dynamic sensors are required and should be installed to activate 12 inches before the top slowdown occurs. The dynamic sensors will function as they always have. If they detect the jacks out of sync more than 3 inches, a resync will occur. If they are more than 6 inches out of sync, the car will shutdown.

Note:	All cars must be installed with the correct top and bottom overtravels